## Slide 1
Strategy flowchart/策略流程 – Generic Applications/通用性应用Generic Assembly Plant process flowchart/通用性主机厂工艺流程:
DBC1200 part enters the Assembly plant preprogrammed with multiple cal blocks/
DBC1200 零件进入装配工厂（内含多个标定软件）
System State “Fault Power On
DTC set for cal block fault
“Cal area NOT Flashed” DTC 158 /系统状态“电源打开错误”
DTC设置标定区错误“标定区未刷新”显示DTC 158
Test Tool unlocks ECU for DID Write / 测试工具解锁ECU 准备DID 写入
Enter programming session/ 进入刷程对话 $10 subfunction /子程序 03 :
710 02 10 03 00 00 00 00 00
790 02 50 03 00 00 00 00 00
Enter Security/进入授权 $27 for DID Write/用于DID 写入 – subfunction /子程序
710 02 27 03 00 00 00 00 00
790 04 67 03 12 34 00 00 00
710 04 27 04 AA BB 00 00 00
790 04 67 04 00 00 00 00 00
Next Page.下一页
Session control / 会话控制
Security
Access / 安全访问
Statement(s)/声明:
“Cal area NOT flashed” DTC158 to set by default / 默认设置DTC158”标定区未刷写”
Can not write DID $FD00 if WSS > 2 kph, NRC $22/ 若轮速大于2kph则无法写入DID $FD00;
Note: 2 or 4 byte seed / key is acceptable (2 byte shown)/注：种子/秘钥为2到4位均可（图中例子为2位）
Active Calibration Block (default)/标定软件激活区 – 16k
Vehicle selectable calibration blocks
Up to 7 versions max /车辆标定软件选择区（最多7个标定文件） - 96k
Application Software block / 应用软件区
Boot Software block / 引导软件区
DBC1200 Memory Architecture/存储器架构

## Slide 2
Strategy flowchart/策略流程 – Generic Applications/通用性应用Generic Assembly Plant process flowchart:
Test Tool reprograms DID $FD00 Bytes 1-6 with SID $2E.
测试工具使用SID $2E再次刷程DID $FD00 1-6字节
Write DID Bytes 1-6/写入DID 1-6字节:
710 07 2E FD 00 11 22 33 44
…. 50ms
790 03 7F 2E 78 00 00 00 00
Note/注: NRC$78 until CAL flash complete（2s-4s between $78_ZOTYE request） /发送否定响应代码$78直至刷写完成（ $78指令之间间隔2-4秒_ZOTYE 要求）
BWI CAL FLASH OCCURS HERE / 此时进行BWI 标定软件刷写
Send Positive response when CAL flash is complete / 标定软件刷写完成时发送肯定响应:
790 03 6E FD 00 11 22 33 44
….
Ecu Resets here / ECU 重启 – No IVC/ESC失去CAN通讯
Statement(s)/声明:
DID write / CAL flash may take up to 3 seconds / DID 写入/标定软件刷写需要约3秒钟；
Programming failure may require BWI to recover part. NRC $72 will be sent in negative response message / 刷程失败可能需要BWI回收零件，此时否定响应指令$72将在信号列表中持续发送。
After ~ 3 sec CAL Flash ECU will then reset / 3 秒刷写完成后ECU 立即重启；
DID Data Validation needs to be worked out. i.e DID Content incorrect/需对DID 数据的确认进行计算。
6. Test tool must send $3E during entire CAL Flash Process/在标定软件刷写期间测试工具需发送
$3E指令
NRC for incorrect DID Content data will be $31 ROOR./对不正确的DID数据的否定响应为$31 ROOR (requestOutOfRange/请求超出范围)
Test Tool tests for correct CAL in ACTIVE block/测试工具对激活区的标定文件进行确认；
DID Write &
Negative Response $78/DID写入&否定响应$78
Note: 1st 4 bytes only shown for simplicity / 注：例子中仅简写了前四个字节
Post Flash of CAL
Test Tool Queries for Active “BWI CAL” Part Number to confirm correct Flash / 测试工具快速刷写 标定软件激活区的“BWI标定”文件件号以确认刷程正确性。
Test Tool Query for CAL Part Number Active/ 测试工具确认标定件号激活
710 03 22 30 04 00 00 00 00
…
790 07 62 30 04 11 22 33 44
ECU Resets after
~ 3 seconds 3秒钟后ECU 重启
ECU sends Positive Response when flash completes/刷写完成时ECU 发送肯定响应
Note: 1st 4 bytes only shown for simplicitysimplicity / 注：例子中仅简写了前四个字节
DID Read for CAL part Number /DID 读取标定文件零件号
Note: 1st 4 bytes only shown for simplicity
Vehicle Calibration Selection/车辆标定选择 DID $FD00 (Read/Write 读写) |  | 
DID Byte Index / DID 字节索引 | Definition / 定义 | Display /显示
#1 | EBCM ECU Calibration Selection Part Number MSB /刷程选择件号M SB | USN / 无符号数
#2 | EBCM ECU Calibration Selection Part Number 2nd MSB/刷程选择件号 2nd MSB | USN / 无符号数
#3 | EBCM ECU Calibration Selection Part Number 2nd LSB/刷程选择件号 2nd LSB | USN / 无符号数
#4 | EBCM ECU Calibration Selection Part Number LSB/刷程选择件号 LSB | USN / 无符号数
#5 | EBCM ECU Calibration Selection Part Number Suffix 1MSB/刷程选择件号尾缀1MSB | ASCII码
#6 | EBCM ECU Calibration Selection Part Number Suffix 2 LSB/刷程选择件号尾缀2LSB | ASCII码
Last Page./上一页

## Slide 3
Strategy flowchart/策略流程 – Generic Applications/通用性应用Vehicle Calibration Select DID $FD00 as defined for Customers /车辆标定数据选择 DID $FD00 根据客户定义
Statement(s)/声明:
A 4 byte seed / key is possible. Application Software only (boot can not support)/可以做4字节的 种子/秘钥，但仅限于应用层软件（引导层软件不支持）
Up to 7 available calibrations are possible for selection to autoflash. / 可支持最多7个标定件号用于选择刷程；
Over 7 calibrations then manual calibration area reprogramming is the only choice. In other words Flash the active cal block only manually with a test tool. / 如多余7个标定软件则只能选择手工刷程（即使用测试工具对激活区进行手工刷写）。
Vehicle Calibration Selection/车辆标定选择 DID $FD00 (Read/Write 读写) |  | 
DID Byte Index / DID 字节索引 | Definition / 定义 | Display /显示
#1 | EBCM ECU Calibration Selection Part Number MSB /刷程选择件号M SB | USN / 无符号数
#2 | EBCM ECU Calibration Selection Part Number 2nd MSB/刷程选择件号 2nd MSB | USN / 无符号数
#3 | EBCM ECU Calibration Selection Part Number 2nd LSB/刷程选择件号 2nd LSB | USN / 无符号数
#4 | EBCM ECU Calibration Selection Part Number LSB/刷程选择件号 LSB | USN / 无符号数
#5 | EBCM ECU Calibration Selection Part Number Suffix 1MSB/刷程选择件号尾缀1MSB | ASCII码
#6 | EBCM ECU Calibration Selection Part Number Suffix 2 LSB/刷程选择件号尾缀2LSB | ASCII码